## Slide 1: Break the Xilence
Elliot Rosen | Jacob Nelson | Stephanie Mao

## Slide 2: Project idea and Motivation
Build a hardware digital synthesizer
  Amplitude envelope
Instant feedback
Out of the ordinary, fun, and interactive project

## Slide 3: Project Goals
Functional
Flexible and responsive (maximum latency < 25ms)
User-friendly

## Slide 4: Where are we now?

## Slide 5: Block Diagram
Software
  Scheduler
Hardware
  Oscillators
  Low Pass Filters
  Multipliers
  Adder
  Digital to Analog Converter

## Slide 6: software
Scheduler
  Receives bytecode from midi controller
  Receives which oscillators are available from hardware
  Interprets bytecode
  Keeps track of unused note banks
  Maps note events to note banks
  Monophonic and Polyphonic?

## Slide 7: Hardware
Implement ADSR envelope
Peripheral control unit control parameters for changes in envelopes which causes varying sounds
Use adder for polyphony

## Slide 8: ADSR envelope
The attack phase starts when a key is pressed
The decay phase follows
The sustain phase lasts as long as the key is pressed
The release phase starts when the key is released
Length of phases determined by peripheral control unit

## Slide 9: Adsr envelope

## Slide 10: Matlab filter simulations

## Slide 11: Digital filter realization
Notes: Digital realization of a direct form 1 digital biquad filter
-z^-1 unit time
-a’s and b’s coefficients

## Slide 12: Where are we really now
Scheduler complete and tested
Oscillators completed and tested
Envelopes complete and being debugged
Filters complete and being debugged
Peripheral controls complete and tested
Note banks almost complete

## Slide 13: What we learned
What not to do:
  Work separately
  All work on the same piece
  Relax too much
What to do:
  Share progress updates with each other
  Divide labor
  Keep common goal specified and in mind

## Slide 14: Our thoughts
Affirmations
Thank you for pushing us early on in the semester
The freedom we were given allowed us to do a cross-disciplinary project
Suggestions
More clear/detailed directions for labs, especially the first one, would’ve been really helpful

## Slide 15: Questions?